## Slide 1: CoSciN Network App
Craig Riecke, CoSciN Network Programmer/Analyst

## Slide 2: The Problem
10 TB
Ithaca
Weill Medical
1 Week!

## Slide 3: Why So Slow?
There are 1GbE bottlenecks in various places
Sharing bandwidth with a lot of campus traffic on older fiber

## Slide 4: Redundant Fiber Promises Fast Paths
Ithaca
Weill

## Slide 5: So Why Not Use Traditional Networking?
One or more new fibers is saturated with Disaster Recovery backup traffic
Path selection (OSPF, BGP, etc.) is not dynamic enough

## Slide 6: Alternate Paths
Ithaca
Weill

## Slide 7: Selecting a Path By Alternate IP
Ithaca
192.168.56.100
Weill
192.168.57.100
192.168.157.100
192.168.159.100
192.168.161.100

## Slide 8: So Why Not Let Client Choose Destination?
They don’t know which path is fastest
The software they’re using (GlobusFTP) ties certs to IP’s.
Difficult to add or remove alternate paths later – requires user training
You’re limited to one path for every transfer

## Slide 9: SDN Can Select the Path For You
Ithaca
192.168.56.100
Weill
192.168.57.100
Src 56.100
Dst 57.100
156.100
157.100
156.100
157.100
56.100
57.100
Policy Based Routing matches (src, dst) with next hops

## Slide 10: How Does App Know Best Path?
Ithaca
192.168.56.100
Weill
192.168.57.100
56.101
157.101
156.101
157.101
156.101
157.101
Sonic
192.168.56.101
Sonic
192.168.57.101
56.101
57.101
Does perfmon on all three paths every 5 minutes

## Slide 11: Problems with Vanilla SDN on HP…
HP executes some Openflow actions in hardware, some in software
IP source and destination modification actions are in software
Software actions are REALLY slow: 8.5 MB/sec. Need about 300 MB/sec

## Slide 12: HP’s New v3 Modules to the Rescue
Can executes more actions in hardware, including IP Rewriting
BUT requires Openflow 1.3, and is really brand-new functionality

## Slide 13: The Default Custom Pipeline Model
Hash Tables: 8K Rows, No Wildcards, Fast
Table 0
VLAN
Eth Src
Table 1
VLAN
Eth Dst
Table 2
IP Src
IP Dst
IP Protocol
TCP/UDP Src Port
TCP/UDP Dst Port
Table 3
Just About Everything
TCAM: 2K Rows, Wildcards, Slightly Slower

## Slide 14: CoSciN Controller Responsibilities
L2 Learning Switch: intranet packets, DHCP, etc.
Cross-Campus Traffic: packets bound for “other” side of CoSciN need path selection and IP rewrites
ARP: routers ask for Mac address of 192.168.156.100 before IP can be rewritten
Path Selection: SONIC servers send current utilization stats

## Slide 15: Handler Architecture
HandlerClass
__init__(nib, logger)
install_fixed_rules(dp)
packet_in(msg)
nib is the network information base shared among all handlers
install_fixed_rules executed on switch connect
packet_in executed on packet in

## Slide 16: Network Information Base (network_information_base.py)
Switches: name, vlan, RYU dp structure including Openflow Datapath ID
Switch attributes: router port, network (e.g. 192.168.56.0/24)
Alternate paths, e.g. 192.168.156.0/24 -> 192.168.157.0/24
Current preferred path
Known Hosts – mac address, port, IP
From configuration file

## Slide 17: L2 Learning Switch – Fixed Rules
Table 0
Table Miss: Goto Controller
Table 1
Table Miss: Flood
Send ARP Request for router Interface, e.g. 192.168.56.1
(Don’t wait for response)

## Slide 18: L2 Learning Switch – Packet In (Host)
Table 0
VLAN = v, Eth Src = s -> Goto 1
Table Miss: Goto Controller
Table 1
VLAN= v, Eth Dst = s -> Output(p)
Table Miss: Flood
If packet is not IP or ARP, just do the actions. Don’t install a rule.
If it is IP or ARP, save mac, IP, and port, and add rule.
If you don’t know port of destination, just flood

## Slide 19: L2 Learning Switch – Packet In (Router)
Table 0
VLAN = v, Eth Src = s -> Goto 2
Table Miss: Goto Controller
Table 1
VLAN= v, Eth Dst = s -> Goto 2
Table Miss: Flood
Table 3
(Cookie: 2000) IP, Eth Src = s -> Goto Controller
(Cookie: 2001) IP, Eth Dst = s -> Goto Controller
Table Miss: Drop
This should probably
be in Cross Campus Handler

## Slide 20: Cross Campus Handler – Packet In (Source Side)
Table 2
(IP src, dst, protocol, source port, dest port) -> Rewrite IP, Output (Router Port)
Set Idle Timeout on this Rule to 5 minutes
Note this is only for CoSciN packets. If bound for internet, add rule without IP rewrite.

## Slide 21: Cross Campus Handler – Packet In (”Target Side”: Cookie: 2001)
Table 2
(IP src, dst, protocol, source port, dest port) -> Rewrite IP, Output (Host Port)
Set Idle Timeout on this Rule to 5 minutes
If we don’t know the host port, don’t add rule. Just rewrite IP and flood. Port will be learned later.

## Slide 22: ARP Handler
Table 3
(Cookie: 3000) ARP-> Goto Controller
Table Miss: Drop
On packet in, if this is an appropriate request, send an ARP reply. Otherwise flood. No rules

## Slide 23: Path Selection Handler
If Ethernet type is 0x808, read the utilization data from the payload
Save the preferred path in NIB. This will get used when creating new flow rules in Table 2

## Slide 24: So How Fast Is It?
280 MB/sec
Traditional networking, no SDN and no IP rewrites: 400 MB/sec

## Slide 25: What OpenFlow Features Could Frenetic Use?
OpenFlow 1.3 Support, forthcoming
Goto table, part of 1.3
Idle Timeouts
Some method for sending rule adds rather than the entire flow table every time.